## Slide 1
Mon CHÉRI ❤️
Mitigating Uninitialized Memory Access with Conditional Capabilities
Merve Gülmez*,†, Håkan Englund*, Jan Tobias Mühlberg‡, Thomas Nyman*
*Ericsson, †DistriNet, KU Leuven, ‡Université Libre de Bruxelles
Merve Gülmez
Ericsson
2025-05-12

## Slide 2: Motivation: Memory Safety
Concerns around memory safety in software industry are increasing thanks to regulatory attention
Memory safety is a combination of correctness aspects which can be improved through a number of means:
Memory-safe programming languages, e.g., Rust
Static and dynamic analysis of unsafe languages
Memory-safe hardware, such as CHERI1: Capability Hardware Enhanced RISC Instruction
Memory-safe hardware particularly attractive for existing code-bases in unsafe languages, such as C and C++
Memory Safety
Resource Safety
Temporal Safety
Type Safety
Data-Race Safety
Spatial Safety
Initialization Safety
[1] J. Woodruff et al., The CHERI capability model: Revisiting RISC in an age of risk, ISCA 2014

## Slide 3: Background: Initialization Safety
Variables that are declared but not given a specific value — a common source of defects in C and C++
    Can lead to subtle, difficult to debug, non-deterministic bugs
    Security issues, if deallocated sensitive data is leaked
Use-before-initialized conditions the fourth largest class of memory-safety vulnerabilities (~10~%)
Memory-safety vulnerabilities
Addressed by Mon CHÉRI
Type safety 14%
Initialization safety 10%
Other 3%
Addressed by CHERI
Spatial safety 44%
Temporal safety 29%
Vulnerability percentages based on 2023 survey by Sutter on CVEs between 2015 – 2022.
❤️

## Slide 4: Capability Hardware Enhanced RISC Instructions
CHERI is an instruction-set extension which replaces conventional pointer with capabilities that enable fine-grained memory protection against many currently widely exploited memory vulnerabilities:
buffer overflows, use-after-free, pointer injection, control-flow attacks

## Slide 5: Our Solution: Conditional Permissions
Conditional permissions are permissions of the form:
𝑿 ⇒ 𝒴 (“𝑿 before 𝒴”)
where permission 𝒴 is granted if operation 𝑿 occurs
On an architectural level (in RISC processors):
operations on memory are limited to load, store (and execute)
permissions on memory are limited to read, write (and execute)
Write-before-read permissions are enforced by ensuring the read permissions of a capability is granted after the capability is used in (at least one) store operation using that capability

## Slide 6: Challenges
How to track conditional permissions for larger areas of memory?
Store “operation bound” for written area and update it each store

## Slide 7: Conditional Capabilities
Operation bounds are updated by hardware in response to 𝑿 operations
Write-before-read update trigged on adjacent write
Address space
Upper bound
permissions
baseline architecture address
object type
bounds
48-bit address
1-bit validity tag
bounds compressed relative to address
Lower bound
Writable memory area
Operation bound
Operation bound
Operation bound
Writable and Readable memory area
Writable and Readable memory area
operation bound

## Slide 8: Challenges
How to track conditional permissions for larger areas of memory?
How to keep track of the additional bound?
Store bound for written area and update it each store
Encode it into the capability

## Slide 9: Operation bound encoding
We extend the CHERI capability format to store additional operational bound in a capability
128-bit representation of Mon CHERI capability
128-bit representation of CHERI capability

## Slide 10: Challenges
How to track conditional permissions for larger areas of memory?
How to keep track of the additional bound?
How to ensure bound in capability is kept consistent throughout its lifetime?
Linearize accesses to use same capability
Store bound for written area and update it each store
Encode it into the capability

## Slide 11: Mon CHÉRI high-level architecture
Conditional capability-enhanced LLVM compiler

## Slide 12: Evaluation: Functional & Performance
Functional: NIST Juliet Test Suite1 for C/C++ evaluated on QEMU full-system emulator
We focus on CWE 457: Use of Uninitialized Variable that consists of 560 Good and 560 Bad test cases
*) False negatives cases exhibits uninitialized behavior, but such behavior that is benign from a security point of view
Performance and Area Cost: Mon CHÉRI is implemented on CHERI-RISC-V FPGA Flute core
only 2%, a small cost considering the overhead of adding CHERI.
a modest ≈ 3.5% overhead over pure-capability mode on Coremark
https://samate.nist.gov/SARD/test-suites/112
 | Positive | Negative
Bad | 560 (100%) | 0 (0%)
Good | 6 (1%)* | 554 (99%)

## Slide 13: Conclusion
We introduce conditional permissions and conditional capabilities for CHERI
We integrate conditional capabilities to CHERI-RISC-V in prototypes based on QEMU full-system emulator and FPGA Flute64Cheri softcore
We add support for Write-before-Read CPs to CHERI-enabled Clang/LLVM compiler and two embedded memory allocators
Evaluation using > 1000 test cases from NIST Juliet test suite and EEMBC CoreMark performance benchmarks showing ≈ 3.5% overhead over CHERI pure-capability mode